## Slide 1
GO1 Quick Guide
Six-slide practical overview for safe setup, operation and maintenance

## Slide 2
Safety and Compliance
The GO1 is a professional quadruped robot, not a toy. Read the manual to understand safety, legal responsibilities, and proper use. Unitree limits warranty and disclaims liabilities; misuse, unauthorized modification, or operation in extreme environments can void coverage and cause damage. Prohibited: disassembly, unauthorized software changes, or operation outside specified conditions; UnitreeRes

## Slide 3
Unpack & Prep
Unpack
Remove packaging and check for shipping damage, dents, leaks, or loose components.
Check Parts
Verify all genuine Unitree parts and connectors are present and undamaged.
Install Battery
Mount the battery pack with the power switch OFF and no power applied.
Level Ground
Place the robot on level ground; abdominal pad flat for stability.
Charge All
Fully charge the remote, tag, and battery pack before first boot.
Update Firmware
Update firmware and app to the latest versions prior to power-on.

## Slide 4
Battery Rules
Key numeric thresholds for safe powering, charging, storage, and protection.
6000–6300
mAh capacity range
21.6–22.2
V nominal voltage
133 Wh
Approx. energy (≈133 Wh)
up to 6 A
Max charge current
25.2 V
Charge target voltage
5–40°C
Charging temperature window (allowed)

## Slide 5
Single Control Only
Ergonomic Bluetooth control with physical buttons for power, mode, and emergency input. Supports follow and joystick modes for direct, tactile control. Switching to a different interface must occur while the robot is stationary to avoid conflicts.
App provides live camera feeds, AI human recognition, and walking controls; Website mirrors the app functions and supports firmware updates. Both interfaces must not control GO1 at the same time to prevent command conflicts.
Only one interface may control GO1 at a time; auto-follow has speed and setup limits to follow safely.

## Slide 6
Terrain Limits
The GO1’s foot assembly uses an air‑compressed pad to sense load and adjust movement. Operate only on open, flat ground and avoid gravel, ice or glass, thick grass or soft foam-like substrates, and environments with debris or dust. Slopes greater than 25° and steps higher than 10 cm pose instability and risk damage. Because it lacks onboard visual perception by default, reduce speed on smootherflo

## Slide 7
Emergency & Warranty
Unstable State
Engage emergency braking only within the protective frame or using the tether/rope.
Joystick Fail
Follow the 'How to turn off when remote fails' procedure in abnormal responses.
Damage Report
Document and photograph damage, then contact Unitree support—shipping costs are user responsibility unless covered.
Warranty Check
If out-of-warranty or excluded (unauthorized modification, water/dust intrusion, non-original battery), expect service fees.
Data Backup
Back up user data before maintenance; do not send severely damaged batteries (they may be rejected).

## Slide 8
Ready for Duty
This GO1 is configured for safe operation across terrain and scenarios. Follow the pre-start checks, battery handling rules, and remote/app control practices to protect performance and preserve warranty. With disciplined care, you’ll maximize uptime, safety, and reliable teamwork with the Unitree GO1.

## Slide 9: Thanks!
Do you have any questions?
youremail@freepik.com
+34 654 321 432
yourwebsite.com
Please keep this slide for attribution